## Slide 1
ArcGIS Desktop Exercise
Using the Montana HUCEnv geodata – Making a Map
The Natural Resource Conservation Service (NRCS) and the Montana State Library NRIS Program (MSL-NRIS) have created geodatabases for 101 8-digit Hydrologic Units (HUCS) or subbasins in Montana that provide environmental datasets clipped to watershed boundaries. Watersheds are useful geographic units for assessing physical, biological, and land use characteristics. These geodatabases can be used for preliminary natural resource inventories, assessments and analysis.
The HUC8_Env geodatabases, metadata, and layer files, are available from http://geoinfo.msl.mt.gov/nrcs_partnership/environmental_characterization
This lesson provides instructions for creating a map and exporting it to a PDF
using the geodata for the Shields Subbasin (HUC 10070003) as an example. Users will first need to download the data for this subbasin along with the ArcMap HUCEnv_Template.mxd and the associated layerfiles.

## Slide 2
Site Assessment
The EARLY BIRD LLC would like to alter a wetland on its property. This exercise will take you through finding the property, exploring multiple datasets on the property, and creating a map in PDF format.
1. With the HUCEnv_Template MXD open in ArcMap, check the box next to the Land Records Layers in the Table of Contents (TOC). Make sure the box next to OwnerParcel (in the Land Records Layers group) is also checked.
2. Right-click on the OwnerParcel layer and select Open Attribute Table.
3. Let’s search by PARCELID to find the property in question. With the attribute table open, click on the Select by Attributes symbol at the top of the attribute table.
4. The Select by Attributes window will open.
Leave the default method as Create a new selection.
Doubleclick on PARCELID in the list of fields and then the equals sign.
Type in the PARCELID number surrounded by single quotes. The query should look like this:
PARCELID = '49140734201080000'
ArcGIS Desktop Exercise
Using the Montana HUCEnv geodata – Making a Map

## Slide 3
5. In the upper left of ArcMap, click on the Zoom to Selected Features button. You can see there is an obvious wetland in the lower center portion of the parcel.
6. It might be useful to know who owns the surrounding properties. Click on the Identify button in the upper left and click on one of the parcels to the left of the property you selected.
The Identify window will open. From the Identify dropdown menu, select OwnerParcel and click on the parcel next to the selected parcel again to see who owns it. We can see the adjoining parcels to the left belong to the same landowner.
ArcGIS Desktop Exercise
Using the Montana HUCEnv geodata – Making a Map

## Slide 4
Let’s explore some of the layers available in the map that might help in assessing the implications of the wetland alteration.
  Check the box next to the Wetland and Riparian Mapping in the TOC. Expand the layer to see the symbology by clicking on the plus sign next to the layer in the TOC.
  You can use the Identify tool by clicking on a wetland or riparian polygon to see what wetland type it is. Choose the Wetland and Riparian Mapping layer in the Identify dropdown menu.
  This parcel is dominated by Riparian Forest and has a freshwater pond with beaver activity, denoted by the “b” in the wetland attribute and described in the “Full Class” field.
  The wetland delineation is from a previous imagery year, but we can still examine the acreage for this polygon to get a general idea.
  In the Identify window, there is a field called ACRES, and we can see that this beaver pond is .39 acres.
Click on the Measure tool to measure the distance between the beaver pond and the nearest road. Choose the unit of measurement in one of the dropdowns on the Measure dialog box.
ArcGIS Desktop Exercise
Using the Montana HUCEnv geodata – Making a Map

## Slide 5
  Turn off the Wetland and Riparian Mapping layer and turn on the SOILS MLRAS Layers. Make sure the MT_MLRAS (statewide) sublayer is checked. Use the Identify tool to find out what the Major Land Resource Area (MLRA) is for this parcel. Use the Identify tool to find out what soil map units are delineated in this area.
  Turn off the MLRA and SOILS_MU layers.
Next turn on the LandCover Layers with the lcmsdi2017 Level 3 sublayer turned on. This is a raster layer consisting of pixels representing different landcover types. By using the Identify tool, we can see that this parcel is dominated by Foothill Riparian Woodland and Shrubland.
Continue to explore other layers in the map that you think will be relevant for your site assessment. Then expand the Aerial Imagery (statewide) layer group and turn off the Natural Color Layers subgroup. Turn on the Color Infrared Layers subgroup. The NAIP_CIR 2017 is on by default.
Color infrared brings out water better than natural color, and the health or type of vegetation is also sometimes more easily distinguishable.
Look at the 2013 and 2015 NAIP CIR to see how the beaver pond has changed from year to year.
We can also use the Swipe tool to look at different layers simultaneously. Click on Customize>Toolbars and select Effects.
In the TOC, turn on both 2015 and 2017 CIR NAIP imagery.
From the dropdown window on the Effects toolbar, select the NAIP_CIR 2015.
Click on the Swipe button on the Effects toolbar and click and drag in the map to see what’s beneath the layer in the dropdown.
ArcGIS Desktop Exercise
Using the Montana HUCEnv geodata – Making a Map

## Slide 6
Making a Map
Click on the layout button at the bottom left of the map.
Decide how large you want your map to be. In this case, we’ll format the layout to be able to print the map to an 11X17 page. Right-click in the white space next to the map and select Page and Print Setup.
Under Size, select 11X17 from the dropdown menu. Check Use Printer Paper Settings as well as Scale Map Elements proportionally to changes in Page Size. Click OK.
Left-click on each half-inch margin to create Guides.
ArcGIS Desktop Exercise
Using the Montana HUCEnv geodata – Making a Map

## Slide 7
5. Use the Select Elements tool to select the map and drag each corner to snap to the Guides you created.
6. From the Standard toolbar, select the Zoom in tool and drag a rectangle around the extent of the parcel to bring it to the forefront.
Most maps have a legend, a title, a scale bar, and a north arrow at a minimum. Let’s add a title first.
From the Insert menu at the top left of ArcMap, select Title.
Using the Select Elements tool, drag the Title box where you want it. Double-click on it to change the text and call this map “Wetland Site Assessment.”
Change the font size and color by clicking on the Change Symbol button.
8. Next insert a north arrow of your choice from the same Insert menu. Place it in a position of your choice in the map.
Do the same for the scale bar.
Next insert the Legend.
Remove all items from the Legend Items window except Wetland and Riparian Mapping by selecting the other layers and clicking the left arrow. Click Next.
Delete the word “Legend” from the Legend Title window and replace it with “Wetland Type”. Click Next.
Click the Background dropdown menu and select Grey 10%. Click Next and Finish.
Now we have a map to Export to a PDF and print.
From the File menu select Export Map and choose PDF under Save as Type. Print the PDF.
ArcGIS Desktop Exercise
Using the Montana HUCEnv geodata – Making a Map

## Slide 8
ArcGIS Desktop Exercise
Using the Montana HUCEnv geodata – Making a Map